## Slide 1: Optimized Tactical Routing for Unmanned Ground Vehicles
CDT Jacob Hyatt
Advisor: LTC Grymes

## Slide 2: Scope
What is the optimal path for an unmanned ground vehicle in a contested environment?
Notes: Talk about how this is a platform developed by clearpath robotics called Moose: Give tech specs

## Slide 3: Previous Work
Walking
Sneaking
Crawling
3
2
4
F
1
S
E
Probability of Detection
Top-Down View
E
Notes: Point out the three layers
Moving around an enemy
Probability of detection increases as you move up layers

## Slide 4: UGV Adaptations
Charging
Not Charging
1
S
2
3
4
F
Probability of Detection
Top-Down View
E
Notes: Taking the framework from the last problem to apply it to UGV
UGV have a set battery charge
UGV has a generator that offsets power use, but increase prob of detection due to noise created
UGV can charge using regenerative braking or a generator

## Slide 5: Methodology
Determine edge costs: detection and energy
Solve multi-objective function
Generate multiple paths for leader consideration
Notes: General Methodology
Multi-objective path function that utilizes detection and energy values
Contour map: introduces the terrain, valley of low vegetation
Detection field: yellow is a higher probability of detection, right on top of enemies means you are detected

## Slide 6: Workflow
1
4
2
5
3
6
Retrieve satellite imagery for AO - USGS and ARCGIS
Generate node field over AO at provided step size - Python
Generate detection and energy edge weights - Python
Write these weights and arcs to file - Python
Utilize Gurobi to run multi-objective optimizer – Julia and JuMP
Utilizing path generate statistics and imagery - Python
Notes: General Methodology
Multi-objective path function that utilizes detection and energy values
Contour map: introduces the terrain, valley of low vegetation
Detection field: yellow is a higher probability of detection, right on top of enemies means you are detected

## Slide 7: Objective Function
Minimize the sum of energy expended and the sum of detection probability for each edge along the path*
Energy Expended: calculated through a drive train simulation
Detection Probability: calculated through visual and audio detection functions
*Simulations modeled using JuMP in Julia and Python and Optimized using the Gurobi solver.
Notes: Point out the two separate equations
Alpha and beta are parameters that can be tuned to change the outcome of the function
Both d_i and E_i have a magnitude between 0 and 1
Minimize the cost function

## Slide 8: Results
Notes: Goes straight through enemies
Minimizes the total number of steps taken

## Slide 9: Results
Notes: Detection moves around enemies

## Slide 10: Results
Notes: Similar to the detection path
Until it diverges
Need to explore why the jagged lines
Hugs the hill to chase changes in elevation

## Slide 11: Next Steps
Further Explore Pareto Frontier
Tweak parameter settings
Extend range
Write Paper

## Slide 12: RFIs
Are the next steps appropriate?
Add the ability to charge in place?
Journal choice?
Division of labor for the paper?

## Slide 13: Even Weight

## Slide 14: Detection

## Slide 15: Battery Charge